## Slide 1: Non-Urban America & the Digital Divide Deep Fiber + New Business Models
Haywood County Broadband Committee
September 12, 2019
Stagg Newman
lsnewmanjr@yahoo.com
828-665-1531

## Slide 2: The Broadband Virtuous Cycle 100 M US. Homes with > 100 Mbps Internet Access in 2020 Non-Urban America Being Left Further Behind!!
Performance doubles Every 2 years in urban and suburban areas
Source: Stagg Newman, FCC Subadvisory Committee work
Telco copper and conventional cellular technology hitting limits; 5G will require 100 times more cell sites per square mile in rural America
Without deep fiber, rural America will be left further behind.
The economics of rural broadband are daunting – and require a fundamental rethinking across Technologies, Local Conditions, and Business Models.
Population Covered | Notional Cost Factor
00% – 90% | 1X-2X
90% - 99% | 2X-20X
99% - 100% | 20X – 200X

## Slide 3: Davis Creek Road Area – Upper Hominy Valley Iconic example of the “Rural” Problem
Charter Spectrum provides 100 Mbps to only 2/3rds homes
ATT exiting market abandoning customers with no or SLOW DSL
Poor cellular coverage due to terrain

## Slide 4: Capital Cost Distribution for Rural FTTH (1000-3000 Households, density 23 HHs/Km2)
Source: https://doi.org/10.1016/j.telpol.2016.04.002
50% of cost is construction of outside plant to the curb
33% of cost is drop to the house
Both of these are dominated by labor costs
The Technologies – Deep Fiber
Sine Qua Non – and it is a civil engineering problem
Insufficient architectures
  Wide area wireless networks without deep fiber
  DSL
  Satellite except for most remote areas
  Older cable networks
Source: Stagg Newman, FCC Subadvisory Committee work

## Slide 5: Future-proof networks Deep Fiber, 5G Wireless, Modern Cable
DIGITAL FIBER
COAX
DEEP FIBER
COAX
R-PHY Node
Source: John Chapman, Cisco. FCC Subadvisory Committee work
Future proof networks
  Deep Fiber down almost all streets
  Final drop by either
    Fiber (fiber to the home)
    Modern cable
    Really high speed wireless
  Robust Mobility
    Cell site radius of ¼ mile or less

## Slide 6: What the Local Communities Can Do Act now to “Bridge the Digital Divide”
  Inventory
  Friendly policies such as dig once, do once for all utilities
  Partnerships including utilities
  RfN for Overbuilds or Upgrades or orchestrate Buy-outs if incumbents will not commit to modernize
  Migigate risks through demand commitment and aggregation and anchor contracts
  Find Partners to create a Deep Fiber Fixed and Mobile Broadband Evolvable Infrastruture
Source: Stagg Newman, FCC Subadvisory Committee work

## Slide 7: Summary
The “Broadband Gap” between rural and underserved areas and urban centers in American is widening rapidly. Costs to close the much larger gap have increased dramatically in the last decade.
Broadband for the vast majority of Americans is on a virtuous cycle with performance doubling every 18 to 36 months continuing to exacerbate the divide.
There is a rich set of technology options that can contribute to solutions but the heart of the problem is overcoming the cost of construction and operations.
New business models and new polices must enable diverse local/regional solutions – because Broadband is increasingly seen as a means for economic well being and as an investment in making rural areas desirable places to thrive.